## Slide 1: Classification of Scheduling Problems
Notes: The scheduling of computer and manufacturing systems has been the subject of extensive research for over sixty years.
In addition to computers and manufacturing, scheduling theory can be applied to many areas including agriculture, hospitals,
transport and others.
<number>

## Slide 2: Scheduling
The scheduling of computer and manufacturing systems has been the subject of extensive research for over sixty years.
In addition to computers and manufacturing, scheduling theory can be applied to many areas including agriculture, hospitals, transport and others.
The main focus is on the efficient allocation of one or more resources to activities over time.
Notes: Adopting manufacturing terminology we use the notions of jobs and machines.
<number>

## Slide 3: Scheduling Problems
Jobs
Machines
1
2
3
Jj ( j = 1, ... , n )
Mk (k = 1, ... , m )
A Schedule is for each job an allocation of one or more time intervals on one or more machines.
Notes: Suppose that m machines … have to process n jobs.
<number>

## Slide 4: Gantt Charts
M3
M3
M2
M2
M2
M1
M1
M1
M1
J3
J2
J3
J2
J1
J1
J3
J1
J4
M1
M2
M3
J1
J2
J3
J4
t
t
0
0
Notes: Schedules may be represented by Gantt charts …
Gantt charts may be machine-oriented or job-oriented
<number>

## Slide 5: Job Data
Ji
Job
Operations
Oi1
Oi2
Oi3
Oi4
M3
M4
Machines
M5
M6
M1
M2
i4
pi4,k
Notes: A job can consist of a number of operations.
A set of machines is associated with each operation Oij.
We assume that Oij may be processed on any of the machines in \muij.
Besides the processing time of operation Oij on machine Mk is given.
<number>

## Slide 6: Dedicated Machines
Ji
Oi1
Oi2
Oi3
Oi4
M3
M4
M1
M2
pi4
All ij are one element sets.
Notes: In our course we will consider the following two basic models.
First when each operation have to be executed on the given machine.
<number>

## Slide 7: Parallel Machines
Ji
Oi1
Oi2
Oi3
Oi4
M3
M4
M1
M2
All ij are equal to the set of all machines.
Notes: Second each operation may be processed on any of all machines.
<number>

## Slide 8: Job Data
pij is a processing requirement associated with operation Oij,
ri is a release date of job Ji.
di is a due date of job Ji.
wi is a weight of job Ji.
fi(t) is a cost function which measures the cost of completing Ji at time t.
Notes: Depending on the problem the following characteristics are given for jobs.
<number>

## Slide 9: Starting and Completion time
si(σ) is the starting time of job Ji in schedule σ.
Ci(σ) is the completion time of job Ji in schedule σ.
Notes: We denote the starting time of job Ji by si()
<number>

## Slide 10: Optimal Schedule
A schedule is feasible if no time intervals on the same machine overlap, if no time intervals allocated to the same job overlap, and if, in addition, it meets a number of problem-specific characteristics.
A schedule is optimal if it minimizes a given optimality criterion.

## Slide 11: |β|γ classification
 specifies the machine environment,
β specifies the job characteristics,
γ denotes the optimality criterion.
Notes: We will discuss a large variety of classes of scheduling problems. These classes are specified in terms of a three-field classification.
<number>

## Slide 12: Job Characteristics
β1 = pmtn indicates that preemption is allowed. Otherwise β1 does not appear in β.
β2 = prec describes precedence relation between jobs.
If β3 = rj then release dates may be specified for each job. If rj = 0 for all jobs then β3 does not appear in β.
β4 specifies restrictions on the processing times or on the number of operations.
If β5 = dj then a deadline dj is specified for each job Ji.
β6 = batch indicates a batching problem.

## Slide 13: Preemption (β1 = pmtn )
Preemption of a job or operation means that processing may be interrupted and resumed at a later time, even on another machine. A job or operation may be interrupted several times.
J3
J2
J3
J2
J1
J1
J4
J1
M1
M2
M3
t
0
s2
C2

## Slide 14: Precedence relations
G = (V,A)
1
3
4
7
8
5
2
6
9
10
(i,k)  A  Ji must be completed
before Jk starts (Ji → Jk).
J3 → J8
J2 → J5
β2 = prec : an arbitrary acyclic directed graph.
Notes: The precedence relations may be represented by an acyclic directed graph …., where V corresponds with the jobs, and
arc (i,k) means that Jj must ………….. In this case we write ……..
<number>

## Slide 15: Batching Problem
A batch is a set of jobs must be processed successively on a machine. The finish time of all jobs in a batch is defined to be equal to the finish time of the last job in the batch.
There is a set up time s for each batch. We assume that this setup time is the same for all batches and sequence independent.
A batching problem is to group jobs into batches and to schedule these batches.
Notes: In some scheduling applications, set of jobs must be grouped into batches.
<number>

## Slide 16: Example of Batching Schedule
0
t
1
2
4
6
5
3
- Set up times
i
- Jobs
C2 = C4 = C6
Batch 2

## Slide 17: Machine Environment
α1 = P : identical parallel machines.
α1 = Q : uniform parallel machines.
α1 = R : unrelated parallel machines.
α1 = F : flow shop.
α1 = O : open shop.
α1 = J : job shop.
If α2 is equal to a positive integer 1, 2, ... then α2 denotes the number of machines.
If α2 = k then k is an arbitrary but fixed number of machines.
If the number of machines is arbitrary we set α2 = ○.

## Slide 18: Identical Parallel Machines
Each job Ji consists of a single operation.
pij = pi for all machines Mj.
J1
J2
M3
M1
M2
p1 = 12
12
12
12
p2 = 18
18
18
18

## Slide 19: Uniform Parallel Machines
Each job Ji consists of a single operation.
pij = pi ∕ sj for all machines Mj.
J1
J2
M3
M1
M2
p1 = 12
12
6
4
p2 = 18
18
9
6
s1 = 1
s1 = 2
s1 = 3

## Slide 20: Unrelated Parallel Machines
Each job Ji consists of a single operation.
Processing time of job can be different on each machine.
J1
J2
M3
M1
M2
12
14
2
10
8
18

## Slide 21: Open Shop
Each job Ji consists of a set of operations.
The machines are dedicated.
There are no precedence relations between operations
Oi1
Oi2
Oi3
Oi4
Ji
M3
M4
M1
M2
Ok1
Ok2
Ok3
Ok4
Jk

## Slide 22: Flow Shop
Each job Ji consists of a set of operations.
The machines are dedicated.
Oi1→ Oi2→ Oi3→...→ Oin for i = 1 ,..., n.
Oi1
Oi2
Oi3
Oi4
Ji
M3
M4
M1
M2
Ok1
Ok2
Ok3
Ok4
Jk

## Slide 23: Feasible Schedules
Oi1
Oi2
Oi3
Oi4
Ok1
Ok2
Ok3
Ok4
Oi1
Oi2
Oi3
Oi4
Ok1
Ok2
Ok3
Ok4
Open
Shop:
Flow
Shop:

## Slide 24: Job Shop
Each job Ji consists of a set of operations.
The machines are dedicated.
Oi1→ Oi2→ Oi3→...→ Oin for i = 1 ,..., n.
Oi1
Oi2
Oi3
Oi4
Ji
M3
M1
M2
Ok1
Ok2
Ok3
Jk

## Slide 25: Total cost function

## Slide 26: Optimality criteria

## Slide 27: Functions depend on due dates

## Slide 28: Some Definitions
An objective function which is monotone with respect to all variables Ci is called regular.
A schedule is called active if it is not possible to schedule jobs (operations) early without violating some constraint.
A schedule is called semiactive if no job (operation) can be processed earlier without changing the processing order or violating the constraints.

## Slide 29: Example 1 (P|prec,pi=1|Cmax)
1
3
4
7
2
5
6
m = 2
1
M1
M2
t
0
4
6
5
3
2
7
Cmax = 5

## Slide 30: Example 2 (1|batch|ΣwiCi)
i | 1 | 2 | 3 | 4 | 5 | 6
pi | 3 | 2 | 2 | 3 | 1 | 1
wi | 1 | 2 | 1 | 1 | 4 | 4
s = 1
0
t
2
3
1
5
4
6
1
4
10
11
15
3
ΣwiCi = 2·3+(1+4+4)·10+(1+4)·15=171

## Slide 31: Example 3 (1|ri; pmtn|Lmax)
i | 1 | 2 | 3 | 4
pi | 2 | 1 | 2 | 2
ri | 1 | 2 | 2 | 7
di | 2 | 3 | 4 | 8
0
t
1
3
4
r1
2
1
r4
r2= r3
d1
d2
d3
d4
Lmax = 4

## Slide 32: Example 4 (J3|pij=1|Cmax)
i j | 1 | 2 | 3 | 4
1 | M1 | M3 | M2 | M1
2 | M2 | M3 |  | 
3 | M3 | M1 |  | 
4 | M1 | M3 | M1 | 
5 | M3 | M1 | M2 | M3
5
M2
M3
t
0
1
4
5
1
3
5
M1
2
5
4
1
3
1
4
2

## Slide 33: Exercises
Suppose γ, γ1 and γ2 are regular objective functions. Which of the following are regular? If you say a function is regular, prove it. If you say otherwise, give an example to show that it is not.
  w1γ1+w2γ2, for w1, w2 > 0.
  γ1– γ2 .
  ecγ, for some c > 0.
  γ1 / γ2 .
Given an instance of J||γ, where γ is a regular objective function, show that there exists an active schedule which is optimal.