## Slide 1: Solid body impact onto a gas-liquid interface
Ermanyuk E.V..
Lavrentyev Institute of Hydrodynamics SB RAS,
Novosibirsk
Dynamics in Siberia
March 2 -6, 2026

## Slide 2: Solid body impact onto a gas-liquid interface
E.V. Ermanyuk
J.-B. Carrat
N.V. Gavrilov
N.D. Shmakova
Lavrentyev Institute of Hydrodynamics SB RAS
Novosibirsk
P. Hicks
University of Aberdeen, UK
R. Purvis
University of East Anglia, Norwich,
UK
M. Ohkusu
Research Institute for Applied Mechanics, Kyushu University, Fukuoka, Japan
A.V. Cherdantsev
Kutateladze Institute of Thermophysics
SB RAS
Novosibirsk
Dynamics in Siberia
March 2 -6, 2026

## Slide 3
Key parameters
Liquid: density, viscosity, surface tension, speed of sound, saturated vapor pressure...
Gas: density, viscosity, speed of sound...
Equations of state for liquid (ideal) and gas (Newtonian liquid)
Nody (impactor): shape, impact speed, mass, stiffness, rugosity, wettability, porosity...
Gravity acceleration
Key non-dimensional numbers:
Weber number
Reynolds number
Ohnesorge number
Capillary number
Stokes number
Density and
viscosity ratios

## Slide 4
Key parameters
Liquid: density, viscosity, surface tension, speed of sound, saturated vapor pressure...
Gas: density, viscosity, speed of sound...
Equations of state for liquid (ideal fluid) and gas (Newtonian fluid)
Nody (impactor): shape, impact speed, mass, stiffness, rugosity, wettability, porosity...
Gravity acceleration neglected
Key non-dimensional numbers:
Weber number
Reynolds number
Ohnesorge number
Capillary number
Stokes number
Density and
viscosity ratios

## Slide 5
Key reviews:
A. A. Korobkin and V. V. Pukhnachev (1988) “Initial stage of water impact,” Annual Rev. Fluid Mech., 20, 159–186
A. L. Yarin (2006) “Drop impact dynamics: Splashing, Spreading, Receding, Bouncing…” Annual Rev. Fluid Mech., 38, 159-192
S. T. Thoroddsen, T. G. Etoh, and K. Takehara (2008) “High-Speed Imaging of Drops and Bubbles” Annual Rev. Fluid Mech., 40, 257-285.
C. Josserand and S. T. Thoroddsen (2016) “Drop Impact on a Solid Surface” Annual Rev. Fluid Mech., 48, 365-391.
D. van der Meer (2017) “Impact on Granular Beds” Annual Rev. Fluid Mech., 49, 463-484.
D. Lohse (2022) “Fundamental Fluid Dynamics Challenges in Inkjet Printing” Annual Rev. Fluid Mech., 54, 349-382

## Slide 6
Length scale D ⁓ O(1 м)÷O(10 м)
ship slamming,
ditching of airplanes and helicopters,
liquid sloshing in oil and LNG carriers....
Points of interest: evaluation of hydrodynamic loading, stress and deformation in structures
Length scale D ⁓ O(0.01 mm)÷O(1 mm)
jet printers (inks, melted alloys), aerosol coating, icing of airplanes, helicopters, ships, wind turbines.....
forensic analysis…
Points of interest: study new physical mechanisms, optimisation of technology ...

## Slide 7
Impact of a flat-nosed body
“…the motion produced by the impact of a flat-nosed body is identical only instantaneously with that (in one half of) the flow field of a flat plate moving through an infinite fluid”
Batchelor G.K. (1967) Introduction to Fluid Mechanics. Cambridge University Press
Fugita (1954),
Chuang (1966),
Verhagen (1967)
In absense of air the body impact at free surface of liquid would produce the water hammer pressure . This pressure has been never observed in experiments. Air density and viscosity cannot be neglected.
Birkhoff G. (1960) Hydrodynamics: a Study in Logic, Facts and Similityde. Princetone University Press.

## Slide 8
Ermanyuk & Ohkusu
(J. Fluids and Structures 2005)
Yakimov (Fluid Dyn 1975)
partial vacuum (13% )
normal atmosphere
Air cushion trapped under the lower disk
no air cushion under the lower disk

## Slide 9
Hydrodynamic loading
μ added mass
where b – submergence of lower point of the body below undisturbed free surface
Two generic cases:
1) constant speed impact
2) speed jump of a flat-nosed body at impact onto free surface
hydrodynamics load
Experimental setup
disc diameter d = 18cm,
radius of bottom curvature:
R = 130 cm concave
R = 130 cm convex
R= ∞ flat
High-speed camera: Motion Xtra HG-100K
Frame rate: 500 to 5000 fps

## Slide 10: Impact speed versus time
Impact height H=5cm, liquid depth h = 6cm
Key principles:
Velocity jump can be evaluated from momentum conservation
Time scale depends on details of the flow geometry.
Momentum conservation:
Batchelor G.K.
Birkhoff G.

## Slide 11: Added muss as function of non-dimensional depth
Chebakov (Appl. Math. Mech. 1974)
flat bottom
concave bottom
convex bottom
Ermanyuk & Gavrilov (J. Appl. Mech. Techn. Phys. 2011)

## Slide 12
Is air trapping persistent for a non-zero deadrise angle?
What is the effect of deadrise angle and impact speed?
Air trapping at normal impact of a flat disk onto a gas-liquid interface

## Slide 13
Flow scheme for a body of “arbitrary” geometry
Impact of wedge / conus onto free surface of liquid
Karman (1929)
Wagner (1932)
T. Karman
H. Wagner

## Slide 14
Schmieden, C. 1953 Der Aufschlag von Rotationskӧrpern auf eine Wasseroberflӓche. ZAMM 33 (4), 147–151.
Wagner, H. 1932 Uber Stoß- und Gleitvorgӓnge an der Oberflӓche von Flüssigkeiten. ZAMM 12 (4), 193–215
Scolan, Y.-M. & Korobkin, A.A. 2001 Three-dimensional theory of water impact. Part 1. Inverse Wagner problem. JFM 440, 293–326.
Scolan, Y.-M. & Korobkin, A.A. 2006 Three-dimensional theory of water impact. Part 2. Linearized Wagner problem. JFM 549, 343–373.

## Slide 15
Scolan, Y.-M. & Korobkin, A.A. 2006 Three-dimensional theory of water impact. Part 2. Linearized Wagner problem. JFM 549, 343–373.
Contact line for a square pyramid
Shape of free surface
at

## Slide 16
Length scale D ⁓ O(0.1mm)÷O(1mm)
E.Q. Li, S.T. Thoroddsen (2015) “Time-resolved imaging of a compressible air disk under a drop impacting on a solid surface” J. Flluid Mech. 780. 636-648.
C. Josserand and S.T. Thoroddsen (2016) “Drop Impact on a Solid Surface” Annual Rev. Fluid Mech., 48, 365-391:
“With 50-ns laser pulses for each video frame, interferometry can be realized at 5 Mfps to obtain the time-resolved evolution of the air-layer profile for higher impact velocities”
Sigurdur
Thoroddsen
126 frames with resolution 800x600
at 7 million fps

## Slide 17
air trapping and
air-bubble formation
Thoroddsen et al.
(JFM 2003)
Problems with measurements for droplet impact
Mani et al. (JFM 2010)
Length scale D ⁓ O(0.1mm)÷O(1mm)

## Slide 18: Air trapping at impact of a sphere onto a gas-liquid interface
Smith, Li & Wu (JFM 2003), Korobkin, Ellis & Smith (JFM 2008), Hicks & Purvis (JFM 2010), Mani, Mandre & Brenner (JFM 2010)
Hicks & Purvis (Phys. Fluids 2011),
Hicks, Ermanyuk, Gavrilov & Purvis (JFM 2012) Hicks & Purvis (JFM 2013)
Approximation:
lubrication regime in thin air layer
+ liquid inertia
Key parameters:
dynamic viscosity of gas,
liquid density,
radius of curvature of body
Experimental setup
Hicks, Ermanyuk, Gavrilov & Purvis (JFM 2012)

## Slide 19
Physical scaling
radius of contact, R – radius of curvature, – penetration depth
added mass of a disk
hydrostatic pressure
inertial pressure
«instantaneous Froude number at small t and large R
Assume that the liquid in the contact zone is forced vie a thin gas lubrication layer of thickness δ, a Insert δ instead of , get scaling for inertial pressure at time scale .
Lubrication pressure in the thin gas layer with dynamics viscosity scales as
Assume
Scaling:
, with Stokes number
Initial radius of the trapped air region scales as

## Slide 20
Air trapping
Radius of curvature R:
80 (∆), 60 (▲), 45 (○), 30 (●) сm
Initial radius of the contact zone
Coefficient in r=CA
C= 3.86 – experimental value
C= 3.8 – calculated value Hicks & Purvis (2010)

## Slide 21: Radius of trapped air domain at impact of a droplet onto a liquid
Mani, Mandre & Brenner (JFM 2010)
Log-log scale
Hicks, Ermanyuk, Gavrilov & Purvis (JFM 2012)
Linear scale
Loss of axial symmetry at low impact speed

## Slide 22: Influence of gass compressibility
Isotermal gas compression :
Mandre, S., Mani, M. & Brenner, M. P. 2009 Precursors to splashing of liquid droplets on a
solid surface // Phys. Rev. Lett. 102 (13), 134502.
Adiabatic gas compression:
Mani, M., Mandre, S. & Brenner, M. P. 2010 Events before droplet splashing on a solid surface // J. Fluid Mech. 647, 163–185.
Parameter of compressibility for adiabatic compression
(Mandre, Mani & Brenner PRL 2009)
C
In Hicks, Ermanyuk, Gavrilov & Purvis (JFM 2012)
this parameter varied between 0.01 and 10

## Slide 23
Improved model with full equation of energy conservation in the gas layer taking into account dependence of gas viscosity on temperature
Hicks P.D. , Purvis R. 2013. “Liquid-solid impacts with compressible gas cushioning”// J. Fluid Mech. 735. 120-149.
Radius of trapped air domain does not depend on air compressibility parameter
Thickness of trapped air domain depends on compressibility parameter and is in a reasonably good agreement with estimates from “adiabatic” gas compression theory.

## Slide 24
Bouwhuis W., Hendrix M.H.W., van der Meer D., Snoeijer J.H. Initial surface deformations during impact on a liquid pool // J. Fluid Mech. 2015. V. 771. P. 503-519.
Typical gas speed at impact of a droplet onto a rigid flat surface
C. Josserand and S.T. Thoroddsen (2016) “Drop Impact on a Solid Surface”
Annual Rev. Fluid Mech., 48, 365-391.
g
varied between 0.01 and 10 (Hicks et al 2012)
and between 5 and 40 (Li & Thoroddsen 2015)

## Slide 25
Visualisation using total internal reflection (TIR)
Jain, Gauthier, van der Meer (Exp Fluids 2021), Jain, Vega-Martinez, van der Meer (JFM 2021)
Experimental setup
Air trapping at impact of a conus onto a liquid

## Slide 27
Trapped air region collapse with formation of a single central air bubble
(blue domain in regime map)
Trapped air region collapse with formation of a gas-bubble necklace
(red domain in the regime map)

## Slide 28
Time-history of outer and inner radii of the wetted area
Outer radius expansion speed (Wagner speed)
(Schmieden, ZAMM 1953)
Karman speed
Outer (inner) radius evolves linearly (exponentially) with time

## Slide 30
Scaling laws for sphere and conus
contact zone radius
added mass of a disk
hydrostatic pressure
inertial pressure
«instantaneous» Froude number
Pressure scale in a sqeeze flow between disks from the lubrication theory for a thin air layer
with dynamic viscosity and thickness δ
Assume
Initial radius of the trapped air region scales as
penetration depth

## Slide 31
Initial radius of trapped air region versus impact speed at different values of the deadrise angle
Initial radius of trapped air region as function of

## Slide 32
  Two liquids with different surface tensions:
    distilled water, мН/м
    2.5% butanol-water solution (BWS), мН/м
  High-speed video:
    1000 to 20000 fps
    resolution 1024 x1024 pixels
Experimental setup
465 мм
470 мм
290 мм
двигатель
Тело
Камера
резервуар

## Slide 33
Regime map for pyramid and conus

## Slide 34
Regime map for wedge

## Slide 36
Square pyramid impact onto gas-liquid interface
«Exotic» patterns
Square «necklace»
Bubbles at square corners
Square donut

## Slide 37
Impact of square pyramid onto gas-liquid interface
Regular case

## Slide 38
Scolan & Korobkin (JFM 2006)
Carrat, Gavrilov, Cherdantsev,
Shmakova, Ermanyuk
(JFM 2026)
“Wagner” contact line
(marked by black arrow)

## Slide 39
“Wagner” radial speed of contact line expansion
π/2 and 4/π – «Wagner» coefficients for wedge and conus, respectively.

## Slide 40
Universal scaling law
for initial size of trapped air film
(wedge, pyramid and conus)

## Slide 42
Scaling parameter
sphere
wedge, conus, pyramid
low sensitivity to variation of input parameters
high sensitivity to variation of input parameters
Combination of two scaling laws allows to control the air trapping:
spherical surface with micro-structure (grooves, pyramides)
pyramid (wedge) with rounded vertex (edge)
Carrat J.-B., Gavrilov N, Cherdantsev A., ShmakovaN., Ermanyuk E. Air entrapment at impact of a conus onto a liquid // J. Fluid Mech. 2023. 966, R1
Carrat J.-B., Gavrilov N, Cherdantsev A., ShmakovaN., Ermanyuk E. Air entrapment at impact of a wedge, pyramide and conus onto a liquid // J. Fluid Mech. 2026.

## Slide 43
Publications:
Carrat J.-B., Gavrilov N, Cherdantsev A., ShmakovaN., Ermanyuk E. Air entrapment at impact of a wedge, pyramide and conus onto a liquid // J. Fluid Mech. 2026.
Carrat J.-B., Gavrilov N, Cherdantsev A., ShmakovaN., Ermanyuk E. Air entrapment at impact of a conus onto a liquid // J. Fluid Mech. 2023.
Cherdantsev A.V., Gavrilov N.V., Ermanyuk E.V. Study of initial stage of entry of a solid sphere into shallow liquid with Synthetic Schlieren technique // Experimental Thermal and Fluid Science. 2021. V. 125. 110375.
Hicks P. D., Ermanyuk E. V., Gavrilov N. V., Purvis R. Air trapping at impact of a rigid sphere onto a liquid // J. Fluid Mech. 2012. V. 695. P. 310–320.
Ерманюк Е.В., Гаврилов Н.В. Экспериментальное исследование падения дисков на мелкую воду // ПМТФ. 2011. Т. 52, № 6. С. 50-57.
Ermanyuk E.V., Ohkusu M. Impact of a disk on shallow water // J. Fluids Structures. 2005. V. 20. No. 3. P. 345–357.

## Slide 44
Thank you for your attention!